## Slide 1: Computing Beyond the End of Moore’s Law
John Shalf
Department Head for Computer Science
Lawrence Berkeley National Laboratory
Numerical algorithms for high-performance computing
April 8-9, 2019
London England
jshalf@lbl.gov

## Slide 2
Atomic scale limit case for 2D Lithography Scaling
2023?
5nm
50

## Slide 3: Is it the end?
“I predict Moore’s Law will never end.
That way I will only be wrong once!”
Alan Kay: Communications of the ACM 1989

## Slide 4: Technology Scaling Trends Exascale in 2021… and then what?
Figure courtesy of Kunle Olukotun, Lance Hammond, Herb Sutter, and Burton Smith
Year
Performance
Transistors
Thread Performance
Clock Frequency
Power (watts)
# Cores
And Then What?
Exascale Happens in 2021-2023
Notes: Thomas said he wouldn’t show this diagram….. OK. I will then.
Well at least we’ve got Moore’s Law (lithography scaling)
But in 2025 we won’t have that any more, and our current play of doubling processor cores that gets us to exascale is no longer going to be available as a source of technology scaling.
Could extend this if you build out in 3D! But energy density is already at the limits, so you cant.
And data movement goes lower if you have photonics or if you have lower voltages….

## Slide 5
New Materials and Devices
20+ years (10 year lead time)
More Efficient Architectures and Packaging
The next 10 years after exascale
Numerous Opportunities Exist to
Continue Scaling of Computing Performance
Many unproven candidates yet to be invested at scale. Most are disruptive to our current ecosystem.
New Models of Computation
Decades beyond exascale
Quantum Computing & others
Hardware Specialization
Post CMOS
Notes: Note: need to work on the

## Slide 6: Alternative Models of Computation
We should adopt an all-in approach

## Slide 7: Beyond Moore Computing Taxonomy
Digital
Quantum
Neuro-
Inspired
Cognitive Computing,
Pattern Recognition
Combinatorial/NP,
Annealing/Optimization,
Simulated Atoms
Symbolic Computation,
Arithmetic,
Logic
Notes: Note: it is true that neural networks are proven to be turing complete
Cat locomotion is an amazing thing… so is their ability to recognize images and play piano.
But Cats suck at adding
They are not so good at solving PDEs
I would not depend on my cat for powerpoint. Quantum Excel (all are affected by lithography). So lets dispense with the idea that if Moore’s law ends, these will replace digital!

## Slide 8: Post CMOS Device Technology
Accelerating the pace for discovery for the future of Microelectronics

## Slide 9: Borkar-Shalf Criteria for New Device Technology
Gain
Signal to Noise
Scalability
Manufacturability
OSTP Report 2015: Together with Robert Leland and Shekhar Borkar

## Slide 10: Comparing CMOS Technology Alternatives
Better
Faster clock rate Slower
Low Energy Intensity High
Nikov & Young
Notes: Formerly the device research community used individual transistor performance parameters
< don’t use pronoun>
Moved to 32 bit adder and it was revolutionary

## Slide 11: Comparing CMOS Technology Alternatives (32 bit adder “benchmark” revolutionized field by focusing effort on device feature improvements that directly benefit the adder)
10x-100x Slower (more parallelism)
Nikov & Young

## Slide 12: Alternatives to Conventional MOS Switches (all require lower clock rate, and much more parallelism)
Today’s CMOS
Technology
Tunneling FET advantage only at low clock rates
Need another 100x parallelism just to maintain status quo!
Notes: There are two take-home messages here:
1) there is no free lunch and no magic (nothing is waiting in the wings to replace CMOS)
2) The things that look promising will require you as a numberical algorithm designer to find another 100x parallelism just to break even
T-FETs improve energy, but increase latency
Can scientific calculations increase parallelism to benefit?
- How much and what kind of parallelism?
Bottom plot says that we can gain big time in energy delay with tfets by sacrificing performance. How to take maximum advantage of such technologies (that sacrifice single core performance).
Many of them push energy delay to slower delay. So more parallelism. How general can we make the advantage? Use John’s diagram for higher delay. Assess this diagram for algorithms that are of scientific importance.
Metrics are: How much does it localize bandwidth density, force you towards higher parallelism. We could use extreme parallelizable algorithms as limit. Very parallel architectures.

## Slide 13: Data Movement Costs: Energy to move data proportional to distance. Power is near chip thermal limits
Energy Efficiency of copper wire:
  Power = Frequency* Length / cross-section-area
  Wire efficiency does not improve as feature size shrinks
Energy Efficiency of a Transistor:
  Power = V2 * frequency * Capacitance
  Capacitance ~= Area of Transistor
  Transistor efficiency improves as you shrink it
Net result is that moving data on wires is starting to cost more energy than computing on said data (interest in Silicon Photonics)
wire
MOS Transistor
Gordon Keeler
DARPA
Notes: Physics is difficult, but at least it appies to us equally
Really at physical limits for off-chip IO power, and physics limits our choices

## Slide 14: DOE Microelectronics BRN (BES, HEP, ASCR)
We need to accelerate the pace of discovery by orders of magnitude
Deep Microelectronics CoDesign Framework

## Slide 15: Multiscale Modeling to accelerate Post-CMOS Development
Materials
Physics
Junction Physics
Device Physics
Length Scale
Compact Models
Analog
Simulation
Characterizing materials, analyzing devices, understanding impacts on circuits, architectures, systems and applications.
Bulk Material:
~100 Atoms
One Junction:
~100k Atoms
One Device:
~1M Atoms
Circuit/Std. Cell:
10-100 Devices
Processor/System:
~10k-1B Circuits
Systems
Architectural
Simulation
Circuits
Current Drive, switching energy, transients
Clock-Rates, Power, Area
Junction Physics,
I-V curves
Material Physics
Carrier Mobility
A holistic end-to-end modeling approach is required
Notes: We can do each of these individual things, but not end to end
We can evaluate a device, but no systematic way of understanding its value in the context of a system

## Slide 16: Gap: Connecting and Scaling
Materials
Physics
Junction Physics
Device Physics
Length Scale
Compact Models
Analog
Simulation
Accelerated feedback path to focus device and material discovery process
Bulk Material:
~100 Atoms
One Junction:
~100k Atoms
One Device:
~1M Atoms
Circuit/Std. Cell:
10-100 Devices
Processor/System:
~10k-1B Circuits
Length Scales
Systems
Architectural
Simulation
Circuits
Switch Speed, Power, Area , Fan-out, Stability
Application Performance
System-Power
Interface-level
Losses/Performance
Materials Metrics
Notes: 30,000 atoms; coarse-graining; boundary-conditions; 10,000 nodes scaling….slow – one junction 1 day.
Junction electronic properties and heat dissipations

## Slide 17: New Breakthroughs in Transistor Technology Require Fundamentally New Principles of Operation
TFET (Tunneling FET): A More sensitive switch Modulated by quantum tunneling instead of thermionic emission
Voltage Range
Off vs On
Over 140 Potential Half-Metals for Experimental Investigation
Notes: Many magnetoelectric/ferroelectric devices: Because of Boltzmann’s Tyrrany
I don’t mean Boltzman has come back from the grave to terrorize us.
Its that as you know, electrons don’t like each other very much. (fundamental limit to current approach to switching transistors
Stuck at 60mV/decade slope to turn the transisoto on and off.
Maybe if we are successful, you won’t have to find another 100x parallelism…

## Slide 18: Results - AND and OR gate in Diode Based Skyrmion
In Collaboration with CXRO – Mi-Young
First Experiment results obtained for primitive logic gates without optimization
Results are superior to state of the art CMOS
Benefits for neuromorphic, or even neuromorphic-based logic gates
Skyrmion Devices
A:0, B:0, Y:0
1
2
A:1, B:0, Y:0
A:0, B:1, Y:0
A:1, B:1, Y:1
3
Y=0
Y=1
Y=0
AND Gate Operation

## Slide 19: Hardware Specialization and the Move Towards Extreme Heterogenous Acceleration
Make Heterogeneous Acceleration Productive for Science

## Slide 20: Extreme Hardware Specialization is Happening Now!
This trend is already well underway in broader electronics industry
Cell phones and even megadatacenters (Google TPU, Microsoft FPGAs…)
(and it will happen to HPC too… will we be ready?)
29 different heterogeneous accelerators in Apple A8 (2016)

## Slide 21: Large Scale Datacenters also Moving to Specialized Acceleration The Google TPU
Deployed in Google datacenters since 2015
“Purpose Built” actually works - Only hard to use if accelerators was designed for something else
Could we use TPU-like ideas for HPC?
Specialization will be necessary to meet energy-efficiency and performance requirements for the future of DOE science!
Model | MHz | Measured Watts |  | TOPS/s |  | GOPS/s /Watt |  | GB/s | On-Chip Memory
 |  | Idle | Busy | 8b | FP | 8b | FP |  | 
Haswell | 2300 | 41 | 145 | 2.6 | 1.3 | 18 | 9 | 51 | 51 MiB
NVIDIA K80 | 560 | 24 | 98 | -- | 2.8 |  | 29 | 160 | 8 MiB
TPU | 700 | 28 | 40 | 92 | -- | 2,300 |  | 34 | 28 MiB
Notional exascale system:
2,300 GOPS/W ? 288 GF/W (dp)  a 3.5 MW Exaflop system!
Notes: Norm Jouppi
5 TF double precision for matrix multiply (if its operating at 100% efficiency)
21 TF half-precision for ML

## Slide 22: The Future Direction for Post-Exascale Computing
Notes: When faced with end of Dennard scaling, the solution was more parallelism
We said we didn’t like that. But in the absence of alterantives, its what industry did. (and dawn of accelerators)

## Slide 23: 3-Pronged Strategy for Post-Exascale Performance Scaling
Hardware Driven Algorithm Design
  Evaluate emerging accelerators in context of workload
  Modify algorithms to take full advantage of new accelerators
Algorithm Driven Hardware Design
  Design accelerators based on algorithm or application requirements
  Use FPGAs for implementation or Lab-led reference design
Co-Develop Hardware and Algorithms
  Design algorithms and hardware together
  Cooperative design with selected industry partner
Specialize Algorithm to Hardware
Hardware
Algorithms and Software
Specialize Hardware to Algorithm
Co-Develop Hardware and Algorithm
Deep knowledge of the mathematics is required to utilize and to design effective accelerators for science
Performance portability is necessary but insufficient…
Notes: Forward Reference the NERSC Strategy  For NERSC
Overlay Nick’s naming convention with this one
And also the superfacility.
Hardware Generators (why it will be affordable)  SystemArchitect and lowering < show the toolkits and hardware generators >
Introduce 3 paths forward -> reference what Kathy said
  HW influence Alg
  Alg influence HW
  Meet in the middle < it is likely to be a bit of both >
Some concluding slide about SW role
  DSLs and other language constructs to make accelerators accessible to DOE science < make something up >

## Slide 24: Example: Redesigning Algorithms for Emerging Accelerators David Keyes has a nice graph that demonstrates this is historically true!
 | Optimization | CPU | + GPU offload
Baseline | Recompile | 0.6x KNL slowdown | Doesn’t work
Code Refactoring | Vectorization, CUDA | 1.8x KNL speedup | 0.9 – 3x
Algorithm Redesign | From 2D to 3D Comm-Avoiding | 0.6 - 27x | 2.5 – 27x
Example: SuperLU optimization paths
Why: optimization alone is insufficient
  Limits to what we can accomplish with code refactoring
How: Algorithm redesign is necessary
Observation: Performance portability only addresses refactoring; larger performance gains rely on algorithm redesign
Notes: Refactor == porting without dramatic change of the algorithm structure.
SuperLU is a sparse LU based direct solver. Performance varies a lot with input matrix sparsity pattern. That’s why I gave a range of speedup numbers.
  Divide expensive Schur-complement update between CPUs & GPUs  3x speedup (2014 - 2015)
  Extensive vectorization on KNL node  80% speedup (2017)
Re-design algorithm: 3D communication-avoiding
  27x speedup, strong scales to 4096 Titan nodes with 4096 GPUs (2018)

## Slide 25: Create Hardware Features to Accelerate Broadly used Numerical Algorithm Primitives Message Queues for low-overhead inter-core communication
Tensilica TIE Queues
Green Flash/Green Wave
OpenSOC Fabric
Chart: Inter-Thread Latency
| Local Exchange | Remote Exchane
x86 | 149.5 | 542.8
RISCV-SoC | 12 | 94
12x
5.7x
Remote Exchange

## Slide 26: Sparse Matrix Trisolve (refresher) Currently Use OMP Atomic to track dependencies

## Slide 27: Example of CoDevelopment of Hardware and Software: SuperLU Dependency Tracking

## Slide 28: Benefit of MsgQ’s on KNL-like architecture
MsgQ TriSolve
OMP TriSolve
OMP limit
4TB/s BW limit
MsgQ can enable a further 20x scaling!
Speedup 2x
Speedup 8x
OpenMP
MsgQ
Algorithm: Redesign SuperLU algorithm to use MsgQ instead of atomics to track dependencies.
Performance:
  12x lower overhead per message than OpenMP
  4x faster than OpenMP for 64cores
  Potential for 8x-20x further scaling
Notes: Current DAG-based methods are unable to hit memory bandwidth peak because of the overhead as you get to finer granularity DAGs
It is also the case that these message queues can be used to accelerate general DAG-based methods
Such as using fast multipole methods

## Slide 29: SNAPPY: Sparse Matrix Compression Accelerator
Spyplot
Visualization
Matrices
Chart: Compression Rates
| A30_015_0_25356 | g7jac160 | matrix-new_3-block8 | xenon1 | copter2 | gas_sensor | shipsec1
LZ | 1.4251 | 1.3998 | 2.1132 | 1.6031 | 1.187 | 1.5658 | 2.0078
Diff then LZ | 1.7181 | 1.7879 | 3.3009 | 1.7379 | 1.3925 | 1.7382 | 2.5288
Chart: Recode BW, 64C, 64 Recode (GB/s)
| A30_015_0_25356 | g7jac160 | matrix-new_3 | xenon1 | copter2 | gas_sensor | shipsec1
Data Rate (64Lane UDP) | 29.0928 | 29.2295 | 20.1067 | 28.8423 | 22.2364 | 27.2668 | 17.9104
64C, 64 UDP Chip | 1861.9366 | 1870.6904 | 1286.8262 | 1845.9084 | 1423.1292 | 1745.0772 | 1146.2634
DR (64b,64L) | 3154.9256 | 3312.6626 | 1843.1928 | 3253.4208 | 2318.3364 | 3065.264 | 1602.7396
DR(14nm,64b,64L) | 5047.8809 | 5300.2601 | 2949.1084 | 5205.4733 | 3709.3382 | 4904.4225 | 2564.3833
Xenon1
Shipsec1
Gas sensor
Copter2
g7jac160

## Slide 30: FFT Design Study With FFTx (Francetti, Popovic, Canning)
For FFT of size N
  Storage = N * operand_size
  Compute = 5/2 * N * log2(N) FLOPs
  Use Pseudo-2D algorithm for large FFTs
Single FFT Accelerator Resource
Assumptions: Spiral HW Generator
  1GHz @ 14nm technology node
  2M point transform (data off-chip)
  HPC Challenge Benchmark: Single precision (Float32) complex, out-of-place
Limit: 100 GB/s off-chip memory
  16k points on-chip engine
  Analytic model for FP limit ~1.5TFLOPs SP
  4.5mm2 area for compute (est.)
Limit: 1TB/s off-chip memory
  ~10k MADD + ~5k add -> 15k FP@1GHz
  Analytical model for FP limit ~15TFLOPs SP
  56mm2 area for compute (est.)
Notes: Note this is configurable: so its not just a fixed FFT… its acceleration of the core elements of an FFT (with some configurability)
That should give you a sense of why current architectures are so gloriously inefficient (how much waste there is)
Apply the apple SOC style to design of HPC chips (compute-intensive kernels are acutaly the worst case)
For memory intensive, I can use on 1mm of chip to saturate all available memory bandwidth (600x more efficient than a GPU… shooting fish in barrel)
Could say to vendor : We know that even if we do crazy Tiling and DAG stuff like Jack and David Keyes, we still call Blas at lowest level
If we limit ourselves to 100 GB/s of off-chip memory bandwidth
  As FFT size grows, so does the Flop/byte ratio
  So large FFT can support 1.5TFLOPs worth of FPUs
  And those FPUs consume just 9mm^2
  Fitting all data on chip is 22mm^2 of SRAM
  But if you go off-chip (100GB/s), you only need 0.007mm^2 of SRAM for registers because temporal recurrences are captured by FPU pipeline stages!
For 1TB/sec of off-chip bandwidth, you can support 15TF of FPUs at 90mm^2 of area
  10x higher performance density than NVIDIA V100GPU (>20x better perf/watt)
  22.5x the performance density of KNL

## Slide 31: FFT Radix 2 RTL generated by SPIRAL – Improved Area, Delay and Performance Model
Chip-layout at 14nm using Mentor Design Synthesis Flow
Shows 2x improved density improvement over analytic model, but 2x lower clock
Floating point multiplier is the Critical path around 1900 ps leading to
  500 MHz design for standard cell based synthesis
  Improved StdCell library (better than OpenSDK) could result in further improvements

## Slide 32: Tiled FFT Performance/Area – NoC + FFT Sim 64 PEs and 256 PEs (best-performing Topology DFly-UGAL)
900GB/s Memory Bandwidth Limit
250 W power limit
~350mm2 area limit (~KNL)
X
~4TFLOP/s SP FFT for 64 PEs NoC ---------- ~15TFLOP/s SP FFT for 256 PE NoC
15x Faster than KNL at 100GB/s -- 7.5x faster than V100 @ 900GB/s
56x higher performance density than KNL – 23x high performance density than V100
X

## Slide 33: Results for RISC-V FFT Accelerator for CryoEM
Created RISC-V Core with FFT ISA Extension
RISC-V+FFT Accel 126x faster than x86 host
  FFT on Intel Core i7-5930K @ 3.50GHz: ~265ms
  FFTAccel (Floating): ~2.10ms
Benchmarking FFT Accelerator for image analysis
Original Image
FFT
Notes: Baseline
Potential benefit
Is it ready yet? (we got this performance on this application… fully synthesized design and its ready to program)

## Slide 34: Example Algorithm-Driven Design of Hardware Accelerators
25%+ of DOE workload is Density Functional Theory (DFT)
What: Design the hardware accelerator around the target algorithm/application
  Purpose-built acceleration
  Lab-led reference design
Why: Huge opportunities to improve performance density and efficiency
  FFT hardware accelerator 50x-100x higher performance density than GPU or CPU+SIMD (using SPIRAL generator)
How: Use Density Functional Theory (DFT) as the target for this experiment
  Large fraction of the DOE workload
  Mature code base and algorithm
  LS3DF formulation minimizes off-chip communication and scales O(N)
Example: LS3DF/Density Functional Theory (DFT)
Notes: Should be < change to 3 bullets >
Selected DFT code for 3 characteristics
1) It’s a huge part of the workload
2) It’s a mature code (doesn’t change often)
3) LS3DF formulation avoids communication and scales O(N)
  Current algorithmic formulation designed to address limits of current SIMD & SIMT requirements
  Must revisit many key algorithm design decisions to make best use of hardware specialization
Opportunities
  O(N) (LS3DF) algorithmic alternative maximizes spatial locality
  FFT accelerator generator (SPIRAL)
  Roll back from “all bands” formulation

## Slide 35: The DFT kernel for each fragment Communication Avoiding LS3DF Formulation – Scales O(N)
O(N2 Log(N))
Comm bound if non-local
O(N3)
Compute-bound
TSQR & Choelesky
One patch per FPGA
400 bands/patch
LS3DF O(N) Algorithm Formulation
Minimizes off-chip Communication
Compute Intensive Kernels
Targeted for HW Specialization
Notes: Key Take-aways
Increase the FLOP density for BLAS and FFT (Spiral)
Minimize data movement (entirely within chip)
And scale with compute rather than adding memory

## Slide 36: Hardware Generators: Enabling Technology for Exploring Design Space Together with Close Collaborations with Applied Mathematics
Chisel
RISC-V
OpenSOC
Open Source Extensible ISA/Cores
Open Source fabric
To integrate accelerators
And logic into SOC
DSL for rapid prototyping
of circuits, systems, and
arch simulator components
Platform for experimentation
with specialization
to extend Moore’s Law
Back-end to synthesize
HW with different devices
Or new logic families
Re-implement processor
With different devices or
Extend w/accelerators
SuperTools
Superconducting
RISC-V
QUASAR
Quantum ISA
Project 38
Multiagency
Architecture
Exploration
Active
Sensors
(talk coming)

## Slide 37: FPGA vs. ASIC
FPGA
ASIC
Cost for first FPGA (NRE): $2,500-$7,500
Cost for 20,000th : $2,500-$7,500
Clock Rate: 0.1-0.3Ghz
Cost for first ASIC (NRE): $2M-$15M
Cost for 20,000th : $150-$250
Clock Rate: 1-2 Ghz (10x)
Area Efficiency: 10x FPGA
Energy Efficiency : 10x-100x FPGA
Notes: If a certain company ever delivers the Stratix 10 FPGAs that they promised various DOE labs last year.
Maybe we could have a program where we prove out accel concepts with sufficiently broad impact, can go to ASIC later.

## Slide 38: Architecture Specialization for Science (hardware is design around the algorithms) can’t design effective hardware without math
Materials
Density Functional Theory (DFT)
Use O(n) algorithm
Dominated by FFTs
FPGA or ASIC
CryoEM Accelerator
LBNL detector
750 GB / sec
Custom ASIC near detector
Genomics Accelerator
String matching
Hashing
2-8bit (ACTG)
FPGA solution
Digital fluid Accelerator
3D integration
Petascale chip
1024-layers
General / special HPC solution
Notes: Project 38  Sherry Li and Sam have been working with us.
Forward Reference to Dave Donofrio Presentation on CryoEM
1) “Nvidia Responds to Google TPU Benchmarking” in HPCWire, April 10, 2017.
2) Scientists engineered a new magnetic ferroelectric at the atomic-scale. A false-colored electron microscopy image shows alternating lutetium (yellow) and iron (blue) atomic planes. An extra plane of iron atoms was inserted every ten repeats, substantially changing the magnetic properties. A major path to reducing energy consumption in digital electronics involves such ferroic materials. Ramamoorthy Ramesh
3. This multi-qubit chip from Irfan Siddiqi’s Lab at UC Berkleey has five superconducting transmon qubits and associated readout resonators. When cooled to absolute zero, such a device can compute things like quantum simulations of advanced materials.

## Slide 39: Software Strategy for Accelerators
Challenge: Current languages are too prescriptive
  Unable to accommodate diverse underlying hardware
  Fundamentally designed for “instruction processors”
Top-Down Strategy : higher level language abstractions
  Raise the level of abstraction for describing algorithms (less prescriptive)
  DSLs (Proto) or hierarchical abstractions in libraries (SuperLU, GraphBLAS) or frameworks (such as AMReX)
  Impact: One description of the algorithm can target multiple accelerators or systems
Bottom-Up Strategy : Application/Algorithm Targeted accelerators
  Create specialized accelerators that target specific algorithms or methods
  Target relatively fixed interfaces and APIs such as FFT, BLAS, or comm.
  Impact: Same accelerator can target multiple applications

## Slide 40: Conclusions
Think more seriously about how to put specialization productively to use for science
  Requires deep understanding of applied mathematics and the underlying algorithms to be successful
Reevaluate the business/economic model for the design and acquisition of HPC systems
Accelerate the development of materials, devices, and systems for post-CMOS electronics

## Slide 41: Beyond-Moore Computing Directions
Heterogeneous Architectures
Specialized accelerators for performance / energy
Post CMOS Devices/Materials
Evaluate new devices using simulation across scales
New Models of Computation
Quantum algorithms, tools and testbeds, for science applications
Workload Analysis, Testbeds, Deployment
Notes: 1) “Nvidia Responds to Google TPU Benchmarking” in HPCWire, April 10, 2017.
2) Scientists engineered a new magnetic ferroelectric at the atomic-scale. A false-colored electron microscopy image shows alternating lutetium (yellow) and iron (blue) atomic planes. An extra plane of iron atoms was inserted every ten repeats, substantially changing the magnetic properties. A major path to reducing energy consumption in digital electronics involves such ferroic materials. Ramamoorthy Ramesh
3. This multi-qubit chip from Irfan Siddiqi’s Lab at UC Berkleey has five superconducting transmon qubits and associated readout resonators. When cooled to absolute zero, such a device can compute things like quantum simulations of advanced materials.

## Slide 42: The End

## Slide 43: Example From SuperLU – Dependency tracking Conversion performed by Yang Liu and Nan Ding
OMP Original Code
Converted to TaskQ
OMP version takes 1 microsecond to perform atomic decrement
Cannot “fire and forget” because next operation is dependent
putQ() operation incurs 5 cycle latency to submit
Requires 5-100 nanoseconds to traverse NoC.
And doesn’t require “find” to scan for work.
Walk list of nodes to search for ”ready” node.
O(N) operation
Poll to immediately return the next available node.
O(k) operation

## Slide 44
MsgQ TriSolve
OMP TriSolve
OMP limit
Recoding Engine limit
MsgQ + Recoding Engine enable even higher concurrencies
MsgQ + Recoding Engine can boost performance by 20x over KNL
4TB/s BW limit

## Slide 45
Benefit of MsgQ’s on KNL-like architecture
MsgQ TriSolve
OMP TriSolve
OMP limit
4TB/s BW limit
MsgQ enables a further 8x scaling!
Blue Line: Conventional OMP scaling
  KNL cores
  OMP time + DGMV/TRSMV time
  OMP limits performance
Green Line: Model for MsgQ Scaling
  KNL cores + MsgQ’s
  MsgQ time + DGMV/TRSMV time
  Assume peak memory BW is 6GB/s/core
MsgQ’s enable 2x better performance than OMP at 64c.
MsgQ’s enable a 512-core KNL architecture with 4TB/s of HBM (8x higher performance) with a 4x better performance than OMP.
Speedup 2x
Speedup 4x
Increases memory bandwidth headroom (now need more BW)

## Slide 46: Example From SuperLU – Dependency tracking Conversion performed by Yang Liu and Nan Ding
OMP Original Code
Converted to TaskQ
OMP version takes 1 microsecond to perform atomic decrement
Cannot “fire and forget” because next operation is dependent
putQ() operation incurs 5 cycle latency to submit
Requires 5-100 nanoseconds to traverse NoC.
And doesn’t require “find” to scan for work.
Walk list of nodes to search for ”ready” node.
O(N) operation
Poll to immediately return the next available node.
O(k) operation

## Slide 47: Message Queue Programming Interface
API
int putQ(uint64_t qid, uint32_t vfunc, uint64_t word);
int putQv(uint64_t qid, uint32_t vfunc, char *v, int len);
  Non-blocking insert word into remote queue for target processor/threadID.
  Return 1 for success, 0 would block (back-pressure), -1 failure
uint64_t waitQ()
  Block for queue activity
  Return qid if item arrived, 0 if timeout or interrupted
uint64_t pollQ()
  Interrogate how many items are in local queue
  Return number of items in queue
int getQ(uint32_t *vfunc, uint64_t &word)
  Pull an item off of the local queue for processing (blocking)
  Return 1 for success, 0 for empty
Example Pseudo Code
Algorithm: triangularSolve (Kale/Charm++)
Input: Row myRows[] Output: Values x[]
if (pollQ() > 0) then
getQ(&vfunc,&msg)
end
for each Row r in independent rows do computeRow(r,0)
end while there are pending rows do
waitQ() // wait for any queue
getQ(&vfunc, &msg)
end
Algorithm 4: Local Triangular Solve

## Slide 48: Multiscale Modeling of Post-CMOS Devices and Systems
Accelerate the discovery of new electronic materials and post-CMOS devices
Notes: Highlight LDRD Investments
Microelectronics BRN
Add one concrete example
MESO
VTA
SpinFPGA
Virtual Fluid
Continuing Digital Computing Performance Scaling Past Moore’s Law
Microelectronics BRN (dates)

## Slide 49: Introduction
Multiple devices, memories, and other “post Moore” technologies in development
Evaluating each option in isolation misses the big picture
    Devices can be better designed with high-level metrics
    Architects can figure out how to best use new technologies
But we lack the tools to do so systematically and rapidly for many technologies
Transistor/Devices
System
Architecture
Notes: Why do we need to do this?

## Slide 50: Joint BES, ASCR, HEP Microelectronics BRN

## Slide 51: Lab-Wide Initiative in Microelectronics (Beyond Moore)
Materials
Physics
Junction Physics
Device Physics
Length Scale
Compact Models
Analog
Simulation
Characterizing materials, analyzing devices, understanding impacts on circuits, architectures, systems and applications.
Bulk Material:
~100 Atoms
One Junction:
~100k Atoms
One Device:
~1M Atoms
Circuit/Std. Cell:
10-100 Devices
Processor/System:
~10k-1B Circuits
Systems
Architectural
Simulation
Circuits
Computing Sciences Focus
Current Drive, switching energy, transients
Clock-Rates, Power, Area
Junction Physics,
I-V curves
Material Physics
Carrier Mobility
A holistic end-to-end modeling approach is required

## Slide 52: Gap: Connecting and Scaling
Materials
Physics
Junction Physics
Device Physics
Length Scale
Compact Models
Analog
Simulation
Accelerated feedback path to focus device and material discovery process
Bulk Material:
~100 Atoms
One Junction:
~100k Atoms
One Device:
~1M Atoms
Circuit/Std. Cell:
10-100 Devices
Processor/System:
~10k-1B Circuits
Length Scales
Systems
Architectural
Simulation
Circuits
Switch Speed, Power, Area , Fan-out, Stability
Application Performance
System-Power
Interface-level
Losses/Performance
Materials Metrics
Notes: 30,000 atoms; coarse-graining; boundary-conditions; 10,000 nodes scaling….slow – one junction 1 day.
Junction electronic properties and heat dissipations

## Slide 53: Ongoing Collaborative Investigations
NCFET
Devices
Components
Architectures
Applications
Magneto Electric
Negative
Capacitance
Quasiparticles

## Slide 54: Beyond-Moore Computing Directions
Heterogeneous Architectures
Specialized accelerators for performance / energy
Post CMOS Devices/Materials
Evaluate new devices using simulation across scales
New Models of Computation
Quantum algorithms, tools and testbeds, for science applications
Workload Analysis, Testbeds, Deployment
Notes: 1) “Nvidia Responds to Google TPU Benchmarking” in HPCWire, April 10, 2017.
2) Scientists engineered a new magnetic ferroelectric at the atomic-scale. A false-colored electron microscopy image shows alternating lutetium (yellow) and iron (blue) atomic planes. An extra plane of iron atoms was inserted every ten repeats, substantially changing the magnetic properties. A major path to reducing energy consumption in digital electronics involves such ferroic materials. Ramamoorthy Ramesh
3. This multi-qubit chip from Irfan Siddiqi’s Lab at UC Berkleey has five superconducting transmon qubits and associated readout resonators. When cooled to absolute zero, such a device can compute things like quantum simulations of advanced materials.

## Slide 55: Backup slides

## Slide 56: Why do chips cost so much?

## Slide 57: Fab and Mask Costs are NOT the Problem
Small (1mm x 1mm) chip tapeouts at 28nm are $14K(US)

## Slide 58: Getting to Critical Mass for IP Reuse for Accelerators

## Slide 59: Sample Application for FFTs: CryoEM
New sensors will overwhelm data transfer and compute facilities
  Data rates exceeding 1 Tb/s
Example from CryoEM : Integrating processing directly into the detector

## Slide 60: RISC-V FFT Accelerator RTL Implementation
Pico RV32I with IMC extensions
RV32IMC accelerator ISA extensions
Programming Interface
Opcode Format
Notes: I – Base RISC-V ISA
M – RISC-V Standard Extension for Integer Multiplication and Division
C – RISC-V Standard Extension for Compressed Instructions

## Slide 61: RISC-V FFT Accelerator API Details
int setupFFT(uint64_t fftid, uint64_t start_address,
uint64_t out_address, uint64_t dim, uint64_t * dimLen);
  Writes dimension, start address, and output address to configuration register file of associated FFT
  Return 1 for success, -1 failure
int startFFT(uint64_t fftid);
  Starts FFT calculation on given fftid
  Return 1 if started, 0 if not
int stopFFT(uint64_t fftid);
  Stops FFT mid-calculation
  Return 1 if stopped, 0 if not
uint64_t getFFTStartAddr(uint64_t fftid);
uint64_t getFFTOutAddr(uint64_t fftid);
uint64_t getFFTDim(uint64_t fftid);
uint64_t * getFFTDimLen(uint64_t fftid);
int getFFTRunStatus(uint64_t fftid);
  Returns values of given configuration values
API

## Slide 62: Example From SuperLU – Dependency tracking Conversion performed by Yang Liu and Nan Ding
OMP Original Code
Converted to TaskQ
OMP version takes 1 microsecond to perform atomic decrement
Cannot “fire and forget” because next operation is dependent
putQ() operation incurs 5 cycle latency to submit
Requires 5-100 nanoseconds to traverse NoC.
And doesn’t require “find” to scan for work.
Walk list of nodes to search for ”ready” node.
O(N) operation
Poll to immediately return the next available node.
O(k) operation

## Slide 63: PARADISE: End-to-End Modelling
Energy
Delay
Application Execution
Current and Voltage Curves
Devices
Circuits
Critical
Path
A
B
A+B
Performance
Logic
Blocks
System
FEEDBACK

## Slide 64: Ongoing Investigations
Collaboration with Material Science Division (MSD) and Centre for X-ray and Optics (CXRO)